The simulation model contains 3 arms.
Each arm contains 3 parts – the swivel, the proximal part, and the distal part.
All this parts are connected to each other by joints, to simulate the arm movement.

Each arm has a servo motor, it applies the movement to the arms by a tendon, that on one side connected to the servo motor, and on the other side is connected to the arm’s parts.

The joint and the tendon, has different constants that can affect the simulation behavior.
You can change the joints damping and stiffness, and for the tendon, you can change its stiffness, range and width

(You can change the tendon damping too, need to determine if it needed)

In the first iteration, this different constants was chosen by changing them randomly and running the simulation until reaching a reasonable result of the arms behavior.
The model constants are described at the table below -

Items	Variable	Current Value
Joints	damping	0.00001
	stiffness	0.00001
Tendon	stiffness	1000
	range	0.1
	Width	0.001

The input of the simulation, is the torque that each motors apply on its tendon.
This inputs (torque) needs to be calibrated against the real inputs of the robot (position probably)

The simulation output will be the relative poistion of the object we decide to manipulate, this output will have to be in the same order as the real robot output.